## Slide 1: Introduction to HPC
Interacting with High Performance Computing Systems
Virginia Trueheart, MSIS
Texas Advanced Computing Center
vtrueheart@tacc.utexas.edu

## Slide 2: An Overview of HPC: What is it?
High Performance Computing
  Parallel processing for advanced computation
  A “Supercomputer”, “Large Scale System”, or “Cluster”
The same parts as your laptop
  Processors, coprocessors, memory, operating system, etc.
  Specialized for scale & efficiency
Scale and Speed
  Thousands of nodes
  High bandwidth, low latency network for large scale I/O
Notes: High Performance Computing most generally refers to the practice of aggregating computing power in a way that delivers much higher performance than one could get out of a typical desktop computer or workstation in order to solve large problems in science, engineering, or business.

## Slide 3: An Overview of HPC: Stampede2
Peak performance: 18 PF, rank 12 in Top 500 (2017)
4,200 68-core Knights Landing (KNL) nodes
1,736 48-core Skylake (SKX) nodes
368,928 cores and 736,512GB memory in total
Interconnect: Intel’s Omni-Path Fabric Network
Three Lustre Filesystems
Funded by NSF through grant #ACI-1134872
Notes: Petaflop a unit of computing speed equal to one thousand million million (1015) floating-point operations per second.
Blue Waters is about 13.34 PF

## Slide 4: An Overview of HPC: Architecture
idev
Internet
ssh
login node
knl-nodes
skx-nodes
sbatch
omnipath
STAMPEDE 2
$HOME
$WORK
$SCRATCH
Notes: What it does on the node will always be faster than on the filesystem bc of the interconnect of omnipath. High throughput low latency. Do things on the node then write out.

## Slide 5: Ex: SKX Compute Node
Model | Intel Xeon Platinum 8160 ("Skylake")
Cores Per Node | 48 cores on two sockets (24 cores/socket)
Hardware Threads per Core | 2
Hardware Threads per Node | 96
Clock Rate | 2.1Ghz
RAM | 192GB
Cache | 57MB per socket
Local Storage | 144GB /tmp partition
Notes: So what does a node look like on a super computer? My Mac here is 1 node with 4 cores and a similar clock rate. The full machine is 4,200 KNL compute nodes AND 1,736 SKX compute nodes.

## Slide 6: Ex: Physical Layout
KNL Node (68 cores per node)
SKX Node (24 cores/socket * 2)
Notes: Technically 72 but due to the way the KNL handles data only 68 are actually “functional” as far as the system is concerned
68 all together or 48 split between two. Different kinds of responses. Figure out what you’re doing and what your code can be made to accommodate

## Slide 7
c455-012[knl](1001)$less /proc/cpuinfo
processor : 0
vendor_id : GenuineIntel
cpu family : 6
model : 87
model name : Intel(R) Xeon Phi(TM) CPU 7250 @ 1.40GHz
stepping : 1
microcode : 0x1ac
cpu MHz : 1496.140
cache size : 1024 KB
physical id : 0
siblings : 272
core id : 2
cpu cores : 68
apicid : 8
initial apicid : 8
fpu : yes
fpu_exception : yes
cpuid level : 13
wp : yes
Notes: What does that look like when im directly on the node and not just theorizing about it? Knl node ex.

## Slide 8
c455-012[knl](1001)$ numactl -H
available: 1 nodes (0)
node 0 cpus: 0 1 2 3 4 5 6 7 8 9 10 11 12 13 14 15 16 17 18 19 20 21 22 23 24 25 26 27 28 29 30 31 32 33 34 35 36 37 38 39 40 41 42 43 44 45 46 47 48 49 50 51 52 53 54 55 56 57 58 59 60 61 62 63 64 65 66 67 68 69 70 71 72 73 74 75 76 77 78 79 80 81 82 83 84 85 86 87 88 89 90 91 92 93 94 95 96 97 98 99 100 101 102 103 104 105 106 107 108 109 110 111 112 113 114 115 116 117 118 119 120 121 122 123 124 125 126 127 128 129 130 131 132 133 134 135 136 137 138 139 140 141 142 143 144 145 146 147 148 149 150 151 152 153 154 155 156 157 158 159 160 161 162 163 164 165 166 167 168 169 170 171 172 173 174 175 176 177 178 179 180 181 182 183 184 185 186 187 188 189 190 191 192 193 194 195 196 197 198 199 200 201 202 203 204 205 206 207 208 209 210 211 212 213 214 215 216 217 218 219 220 221 222 223 224 225 226 227 228 229 230 231 232 233 234 235 236 237 238 239 240 241 242 243 244 245 246 247 248 249 250 251 252 253 254 255 256 257 258 259 260 261 262 263 264 265 266 267 268 269 270 271
node 0 size: 98207 MB
node 0 free: 91727 MB
node distances:
node 0
0: 10
Notes: Non-uniform memory access (NUMA) is a computer memory design used in multiprocessing, where the memory access time depends on the memory location relative to the processor.
This is another way to visualize it. Each of these is a “logical cpu” rather than a physical cpu. Bc we have hyper threading turned on you can run 4 threads on every core resulting in a total possible 272 tasks if you are very very careful. Generally we see better results with 64> physical cores used. Hardware threads = physical cores, software threads = logical cores. Threads, tasks, cores, etc. we have 8 different names for the same things.

## Slide 9: An Overview of HPC: Using a System
Why would I use HPC resources?
  Large scale problems
  Parallelization and Efficiency
  Collaboration
How do I find an HPC resource?
  Check with your institution
  Check with national scientific groups (NSF in the US)
Notes: You’re working on climate data so your problem sets are huge. How many years? How granular? Do you want to develop visualizations? Predictive scaling? We could track Harvey in real time and predict where the deepest water was after the fact to help rescue crews manage their responses. We also kept legacy data for future study.
Application processes, depending on their model access may be free but access is in high demand so you have to prove that you’ll be doing valuable science on the machine

## Slide 10: Overview: What Can I Find on a System
Modules and Software
  Basic compilers and libraries
  Popular packages
  Licensed software
Build Your Own!
  github or other direct sources
  pip, wget, curl, etc
  You won’t have sudo access

## Slide 11: What Do I Need to Get Started?
User Account
Allocation & Project
Two Factor Authentication
Notes: Now that you know a bit about what HPC systems involve, let’s try it out. What do I need to get started?

## Slide 12: Please See Your Handouts!
Username
Password
Temporary TFA Key
Notes: Ok, let’s get started!

## Slide 13: SSH Protocols
Secure Shell
  Encrypted network protocol to access a secure system over an unsecured network
  automatically generated public-private key pairs
  Your Wi-Fi Stampede2 or other secure machine
  File transfers (scp & rsync)
Options
  .ssh/config
  Host & Username
  Make connecting easier
  Passwordless Login
Notes: We’ll come back to complex options later in the customizing your environment section. Programmers are lazy we don’t want to type more than we have to. On windows PuTTY is a ssh client

## Slide 14: Logging In (Mac Terminal)
$ ssh <username>@stampede2.tacc.utexas.edu
To access the system:
If not using ssh-keys, please enter your TACC password at the password prompt
At the TACC Token prompt, enter your 6-digit code followed by <return>.
Password:
TACC Token Code:
Notes: Inputs at password and token will likely appear blank so type carefully

## Slide 15: Logging in (PuTTY pt. 1)
Notes: If this doesn’t work in putty you may need to update settings on your machine:
In Settings app, go to Apps > Apps & features > Manage optional features.
Locate “OpenSSH server” feature, expand it, and select Install.

## Slide 16: Logging in (PuTTY pt. 2)

## Slide 17
Welcome to Stampede2, *please* read these important system notes:
--> Stampede2, Phase 2 Skylake nodes are now available for jobs
--> Stampede2 user documentation is available at:
https://portal.tacc.utexas.edu/user-guides/stampede2
----------------------- Project balances for user vtrue -----------------------
| Name Avail SUs Expires | |
| A-ccsc 189624 2018-12-31 | |
------------------------- Disk quotas for user vtrue --------------------------
| Disk Usage (GB) Limit %Used File Usage Limit %Used |
| /home1 1.9 10.0 19.43 39181 200000 19.59 |
| /work 311.8 1024.0 30.45 225008 3000000 7.50 |
| /scratch 0.0 0.0 0.00 4 0 0.00 |
-------------------------------------------------------------------------------

## Slide 18: Where am I?
Login Nodes
  Manage files
  Build software
  Submit, monitor and manage jobs
Compute Nodes
  Running jobs
  Testing applications

## Slide 19
Welcome to Stampede2, *please* read these important system notes:
--> Stampede2, Phase 2 Skylake nodes are now available for jobs
--> Stampede2 user documentation is available at:
https://portal.tacc.utexas.edu/user-guides/stampede2
----------------------- Project balances for user vtrue -----------------------
| Name Avail SUs Expires | |
| A-ccsc 189624 2018-12-31 | |
------------------------- Disk quotas for user vtrue --------------------------
| Disk Usage (GB) Limit %Used File Usage Limit %Used |
| /home1 1.9 10.0 19.43 39181 200000 19.59 |
| /work 311.8 1024.0 30.45 225008 3000000 7.50 |
| /scratch 0.0 0.0 0.00 4 0 0.00 |
-------------------------------------------------------------------------------

## Slide 20: Allocations
Active Project with a Project Instructor attached
Service Units (SUs)
  SUs billed (node-hrs) = ( # nodes ) x (wall clock hours ) x ( charge rate per node-hour )
Shared Systems
  Be a good citizen

## Slide 21
Welcome to Stampede2, *please* read these important system notes:
--> Stampede2, Phase 2 Skylake nodes are now available for jobs
--> Stampede2 user documentation is available at:
https://portal.tacc.utexas.edu/user-guides/stampede2
----------------------- Project balances for user vtrue -----------------------
| Name Avail SUs Expires | |
| A-ccsc 189624 2018-12-31 | |
------------------------- Disk quotas for user vtrue --------------------------
| Disk Usage (GB) Limit %Used File Usage Limit %Used |
| /home1 1.9 10.0 19.43 39181 200000 19.59 |
| /work 311.8 1024.0 30.45 225008 3000000 7.50 |
| /scratch 0.0 0.0 0.00 4 0 0.00 |
-------------------------------------------------------------------------------

## Slide 22: Filesystems
Division of Labor
  Linux Cluster (Lustre) system that look like a single hard disk space
  Small I/O is hard on the system
  Striping large data (OST, MDS)
Partitions
  $HOME: 10GB, $WORK: 1TB, $SCRATCH: Unlimited
  Shared system
Notes: Object storage target and metadata server

## Slide 23
Notes: Performance increases with filesystem size. But there are also caveats for long term storage associated with these resources

## Slide 24: Filesystems: Cont.
Where am I?
  pwd – print working directory
  cd – change directory
  cd .. – move up one directory
New Files
  mkdir – make directory
  Editors – vi(m), nano, emacs
  mv – move a file to another location
Notes: This is a rehash of Saturday but it will help you move around in what we’re going to do next

## Slide 25: Create a File
login1.stampede2$ cd $WORK
login1.stampede2$ pwd
/work/03658/vtrue/stampede2
login1.stampede2$ nano helloWorld.py

## Slide 26: A Very Small File
#!/usr/bin/env python
"""
Hello World
"""
import datetime as DT
today = DT.datetime.today()
print "Hello World! Today is:"
print today.strftime("%d %b %Y")

## Slide 27: Run an Interactive Job
idev
  Interactive development queue access command
  Watch your code run live
  Test things in real time
  idev –help for options
idev will drop you directly into the knl development queue so be aware of your location on the system.

## Slide 28: helloWorld.py
staff.stampede2(1005)$ idev
-> Checking on the status of development queue. OK
-> Defaults file : ~/.idevrc
-> System : stampede2
-> Queue : development (idev default )
[...]
c455-012[knl](1019)$
Notes: Pay attention to your command prompt. Ofc you can change this if you want but many systems have a default that is designed to be helpful .

## Slide 29: helloWorld.py
staff.stampede2(1005)$ idev
-> Checking on the status of development queue. OK
-> Defaults file : ~/.idevrc
-> System : stampede2
-> Queue : development (idev default )
[...]
c455-012[knl](1019)$ python helloWorld.py
Hello World! Today is:
17 Jun 2018
c455-012[knl](1020)$
Notes: Single processor

## Slide 30: Types of Code
Serial Code
  Albeit a very, very small one
  Single tasks, one after the other
  Single node/single core
Parallel Code
  Array or “embarrassingly parallel” jobs
  Many node/many core
  Uses MPI
  Hybrid codes
Notes: We’ll get to multithreading in a minute and how that actually works vs hyperthreading
A lot of people will use the fact that there are more cores on a node some people will run across it repeatedly for more through put

## Slide 31: Message Passing Interface
ibrun is TACC specific
  “Wrapper” for mpirun
  Execute serial and parallel jobs across the entire node
MPI Functions
  Allows communication between all cores and all nodes
  Move data between parts of the job that need it
  Point-to-Point or Collective Communication
Notes: Point to point is communication between to processes so task 1 on core 1 talks to core 2 etc. Collective communication implies a synchronization point. All of your tasks much get to a certain point before moving to the next step (barrier) or broadcast, from single point send out the same data to other processors. You can get super fancy with this and build tree structures to help your code. Paired things like vectorization this becomes very important for increasing the performance of your code at a larger scale.

## Slide 32: Ex: MPI Communication
Point-to-Point
Collective
proc 0
proc 1
proc 2
proc 3
proc 4
proc 0
proc 3
proc 7
proc 4
proc 9
Notes: You can do this for as many logical cores are on the node or you can do it between nodes. But specify which you’re doing in your code or your just going to trip it up.
Point to point can be send/receive or a send or a receive separately and can go between any single core. This can be in order or not but its not the same thing being pushed out across multiple cores that is a “broadcast” the reverse can be “gathering” as in scatter and gather

## Slide 33
#!/usr/bin/env python
"""
Parallel Hello World
"""
from mpi4py import MPI
import sys
size = MPI.COMM_WORLD.Get_size()
rank = MPI.COMM_WORLD.Get_rank()
name = MPI.Get_processor_name()
sys.stdout.write(
"Hello, World! I am process %d of %d on %s.\n"
% (rank, size, name))
Notes: Single node/task = one output
Shift + ZZ to save and exit
ls to see if file was saved
We’ll come back for this later when we start running some examples but for now make sure it’s saved and try to remember where you put it

## Slide 34: Parallel helloWorld.py
c455-012[knl](1019)$ ibrun python helloParallel.py
TACC: Starting up job 1595632
TACC: Starting parallel tasks...
Hello, World! I am process 1 of 68 on c456-042.stampede2.tacc.utexas.edu.
Hello, World! I am process 49 of 68 on c456-042.stampede2.tacc.utexas.edu.
Hello, World! I am process 66 of 68 on c456-042.stampede2.tacc.utexas.edu.
Hello, World! I am process 67 of 68 on c456-042.stampede2.tacc.utexas.edu.
Hello, World! I am process 64 of 68 on c456-042.stampede2.tacc.utexas.edu.
...
TACC: Shutdown complete. Exiting.
Notes: Single processor per task (multithreaded) but not yet hyperthreaded
Great! Now you know how to run jobs interactively

## Slide 35: Submitting a Job
Why submit?
  Larger jobs, more nodes
  You don’t have to watch it in real time
  Run multiple jobs simultaneously
Queues
  Pick the queues that suit your needs
  Don’t request more resources than you need
  Remember this is a shared resource
Never run on a login node!
Notes: So many more options available. What’s available? See the queues!

## Slide 36
Queue Name | Node Type | Max Nodes per Job | Max Duration | Max Jobs in Queue | Charge Rate
development | KNL cache-quad | 16 nodes | 2hrs | 1 | 1SU
normal | KNL cache-quad | 256 nodes | 48hrs | 50 | 1SU
large** | KNL cache-quad | 2048 nodes | 48hrs | 5 | 1SU
long | KNL cache-quad | 32 nodes | 96hrs | 2 | 1SU
flat-quadrant | KNL flat-quad | 24 nodes | 48hrs | 2 | 1SU
skx-dev | SKX | 4 nodes | 2hrs | 1 | 1SU
skx-normal | SKX | 128 nodes | 48hrs | 25 | 1SU
skx-large** | SKX | 868 nodes | 48hrs | 3 | 1SU
Notes: Varies based on the number of nodes the system has and the frequency of use. Large queues are special as they take up so much of the system and a poorly run job could a) cause system problems b) cost you a lot of SUs that you wont get refunded.
Cache-quad and flat-quad has to do with the way memory is distributed. We keep most of the knl’s in cache bc the response time is faster but sometimes that means there is less room for certain operations. If your code is heavier on the memory switch to flat quad so you can get the full memory available. Instead of 16+96 you get 112GB flat.
Cache Mode. In this mode, the fast MCDRAM is configured as an L3 cache. The operating system transparently uses the MCDRAM to move data from main memory. In this mode, the user has access to 96GB of RAM, all of it traditional DDR4. Most Stampede2 KNL nodes are configured in cache mode.
Flat Mode. In this mode, DDR4 and MCDRAM act as two distinct Non-Uniform Memory Access (NUMA) nodes. It is therefore possible to specify the type of memory (DDR4 or MCDRAM) when allocating memory. In this mode, the user has access to 112GB of RAM: 96GB of traditional DDR and 16GB of fast MCDRAM. By default, memory allocations occur only in DDR4. To use MCDRAM in flat mode, use the numactl utility or the memkind library; see Managing Memory for more information. If you do not modify the default behavior you will have access only to the slower DDR4.

## Slide 37: Submitting a Job cont.
sbatch
  Simple Linux Utility for Resource Management (SLURM)
  Linux/Unix workload manager
  Allocates resources
  Executes and monitors jobs
  Evaluates and manages pending jobs
Using a Scheduler
  Gets you off of the login nodes (shared resource)
  Means you can walk away and do other things
Notes: This is how the system knows what’s trying to run. Helps manager resources and tries to keep things “fair” is generally automated though can be manipulated by admins.

## Slide 38: Submission Options
Option | Argument | Comments
-p | queue_name | Submits to queue (partition) designated by queue_name
-J | job_name | Job Name
-N | total_nodes | Required. Define the resources you need by specifying either: (1) "-N" and "-n"; or (2) "-N" and "--ntasks-per-node".
-n | total_tasks | This is total MPI tasks in this job. When using this option in a non-MPI job, it is usually best to set it to the same value as "-N".
-t | hh:mm:ss | Required. Wall clock time for job.
-o | output_file | Direct job standard output to output_file (without -e option error goes to this file)
-e | error_file | Direct job error output to error_file
-d= | afterok:jobid | Dependency: this run will start only after the specified job successfully finishes
-A | projectnumber | Charge job to the specified project/allocation number.
Notes: This isn’t all options but it covers the most commonly used ones and the ones that are required. You have to tell the system what you are trying to do and this is how you communicate with it via the work load manager.

## Slide 39: Parallel Job
#!/bin/bash
#SBATCH -J myJob # Job name
#SBATCH -o myJob.o%j # Name of stdout output file
#SBATCH -e myJob.e%j # Name of stderr error file
#SBATCH -p development # Queue (partition) name
#SBATCH -N 1 # Total # of nodes
#SBATCH -n 68 # Total # of mpi tasks
#SBATCH -t 00:05:00 # Run time (hh:mm:ss)
#SBATCH -A myproject # Allocation name (req'd if you have more than 1)
# Other commands must follow all #SBATCH directives...
module list
pwd
date
# Launch code...
ibrun python helloParallel.py
Notes: “slurm batch”

## Slide 40: Managing Your Jobs
qlimits – all queues restrictions
sinfo – monitor queues in real time
squeue – monitor jobs in real time
showq – similar output to squeue
scancel – manually cancel a job
scontrol – detailed information about the configuration of a job
sacct – accounting data about your jobs

## Slide 41
staff.stampede2(1009)$ squeue -u vtrue
JOBID PARTITION NAME USER ST TIME NODES NODELIST(REASON)
1604426 development idv20717 vtrue R 16:57 1 c455-001
staff.stampede2(1010)$ scontrol show job=1604426
JobId=1604426 JobName=idv20717
UserId=vtrue(829572) GroupId=G-815499(815499) MCS_label=N/A
Priority=400 Nice=0 Account=A-ccsc QOS=normal
JobState=RUNNING Reason=None Dependency=(null)
Requeue=0 Restarts=0 BatchFlag=1 Reboot=0 ExitCode=0:0
RunTime=00:18:08 TimeLimit=00:30:00 TimeMin=N/A
SubmitTime=2018-06-09T21:27:33 EligibleTime=2018-06-09T21:27:33
StartTime=2018-06-09T21:27:36 EndTime=2018-06-09T21:57:36 Deadline=N/A
PreemptTime=None SuspendTime=None SecsPreSuspend=0
LastSchedEval=2018-06-09T21:27:36
...

## Slide 42: Accessing a Compute Node
No Job Running
staff(1003)$ ssh c455-001
Access denied: user vtrue (uid=829572) has no active jobs on this node.
Authentication failed.
Job Running
staff(1002)$ ssh c455-032
Last login: Fri Jun 15 15:46:04 2018 from staff.stampede2.tacc.utexas.edu
TACC Stampede2 System
Provisioned on 24-May-2017 at 11:49
c455-032[knl](1001)$

## Slide 43: On Node Monitoring
cat /proc/cpuinfo
  Follow a read out of the cpu info on the node
top
  See all of the processes running and which are consuming the most resources
free –g
  Basic print out of memory consumption
Remora
  This is an open source tool developed by TACC that can help you track memory, cpu usage, I/O activity, and other options

## Slide 44: What else is on the Login Node?
Modules
  Find software, compilers, dependent packages
Environments
  Paths, personalizations, licenses
Building Software
  Install what you need, compile, update
Notes: Lua based module system. A modulefile contains the necessary information to allow a user to run a particular application or provide access to a particular library. All of this can be done dynamically without logging out and back in. Modulefiles for applications modify the user's path to make access easy. Modulefiles for Library packages provide environment variables that specify where the library and header files can be found. It is also very easy to switch between different versions of a package or remove the package.
Module -help

## Slide 45: Modules
Modules
  TACC uses a tool called Lmod
  Add, remove, and swap software packages
  Saves you from having to build your own
Commands
  module spider <package> - search for a package
  module list – see currently loaded modules
  module avail – list all available packages
  module load <package> - load a specific package or version
Notes: Lua based module system. A modulefile contains the necessary information to allow a user to run a particular application or provide access to a particular library. All of this can be done dynamically without logging out and back in. Modulefiles for applications modify the user's path to make access easy. Modulefiles for Library packages provide environment variables that specify where the library and header files can be found. It is also very easy to switch between different versions of a package or remove the package.
Module -help

## Slide 46
staff.stampede2(1073)$ module list
Currently Loaded Modules:
1) intel/17.0.4 2) impi/17.0.3 3) git/2.9.0 4) autotools/1.1 5) xalt/1.7.7 6) TACC 7) python2/2.7.14
staff.stampede2(1078)$ module spider python
----------------------------------------------------------------------------------------
python:
----------------------------------------------------------------------------------------
Versions:
python/2.7.13
Other possible modules matches:
python2 python3
----------------------------------------------------------------------------------------
To find other possible module matches execute:
$ module -r spider '.*python.*'
Notes: Suggestions. READ!! It will often tell you what you need to know about the package

## Slide 47
staff.stampede2(1073)$ module spider python3/3.6.4
------------------------------------------------------------------------------------- python3: python3/3.6.4
------------------------------------------------------------------------------------- Description:
scientific scripting package
You will need to load all module(s) on any one of the lines below before the "python3/3.6.4" module is available to load.
intel/17.0.4
Help:
This is the Python3 package built on March 01, 2018.
You can install your own modules (choose one method):
1. python3 setup.py install --user
2. python3 setup.py install --home=<dir>
3. pip3 install --user module-name
Version 3.6.4
Notes: Suggestions. READ!! It will often tell you what you need to know about the package
We’ll address some more commands later …like squeue etc

## Slide 48: Environment Management
env – Read out of all the environment variables set
Look for something specific:
staff.stampede2(1017)$ env | grep GIT
TACC_GIT_BIN=/opt/apps/git/2.9.0/bin
TACC_GIT_DIR=/opt/apps/git/2.9.0
TACC_GIT_LIB=/opt/apps/git/2.9.0/lib
GIT_TEMPLATE_DIR=/opt/apps/git/2.9.0/share/git-core/templates
GIT_EXEC_PATH=/opt/apps/git/2.9.0/libexec/git-core

## Slide 49: Environment Paths
$echo $PATH
/opt/apps/xalt/1.7.7/bin:/opt/apps/intel17/python/2.7.13/bin:/opt/apps/autotools/1.1/bin:/opt/apps/git/2.9.0/bin:/tmprpm/intel17/impi/17.0.3/bin:/opt/intel/compilers_and_libraries_2017.4.196/linux/mpi/intel64/bin:/opt/intel/compilers_and_libraries_2017.4.196/linux/bin/intel64:/opt/apps/gcc/5.4.0/bin:/usr/lib64/qt-3.3/bin:/usr/local/bin:/bin:/usr/bin:/opt/dell/srvadmin/bin:.
$echo $LD_LIBRARY_PATH
/opt/apps/intel17/python/2.7.13/lib:/opt/intel/compilers_and_libraries_2017.4.196/linux/mpi/intel64/lib:/opt/intel/debugger_2017/libipt/intel64/lib:/opt/intel/debugger_2017/iga/lib:/opt/intel/compilers_and_libraries_2017.4.196/linux/tbb/lib/intel64_lin/gcc4.4:/opt/intel/compilers_and_libraries_2017.4.196/linux/daal/lib/intel64_lin:/opt/intel/compilers_and_libraries_2017.4.196/linux/tbb/lib/intel64/gcc4.7:/opt/intel/compilers_and_libraries_2017.4.196/linux/mkl/lib/intel64_lin:/opt/intel/compilers_and_libraries_2017.4.196/linux/compiler/lib/intel64_lin:/opt/intel/compilers_and_libraries_2017.4.196/linux/ipp/lib/intel64:/opt/intel/compilers_and_libraries_2017.4.196/linux/compiler/lib/intel64:/opt/apps/gcc/5.4.0/lib64:/opt/apps/gcc/5.4.0/lib
Notes: These are the two most important things to keep track of where the system looks for executables and libraries. The order of these _matters_ it will pick what it finds first and stick with it and ignore subsequent matching pieces. You can change these to accommodate installing new software but be careful.

## Slide 50: Diagnosing Your Environment
$module load sanitytool
$sanitycheck
Sanity Tool Version: 1.3
1: Check SSH permissions:
Passed
2: Check SSH keys:
Passed
3: Check environment variables (e.g. HOME, WORK, SCRATCH) and file system access:
Passed
...
Notes: If anything is no correct it will say “FAILED” and then provide you with instructions

## Slide 51: .bashrc (or shell appropriate script)
Set default modules
Set custom paths permanently
Change command line prompt
Set aliases
Change Umask settings for sharing files
Enable startup script tracking
Notes: Show live demo for this

## Slide 52
alias priority='squeue -t pending -o "%Q %.7i %.9P %.8j %.2t %.10M %.6D %r %B %S" --sort="-p"'
alias qalloc='squeue -A UT-2015-05-18 -o "%.18i %.9P %.9G %.16a %.6D %.20S %.8M %.10L %.10Q"'
alias qalloct='squeue -i 5 -A UT-2015-05-18 -o "%.18i %.9P %.9G %.16a %.8u %.6D %.20S %.8M %.10L
%.10Q"'
alias tacc_jobs='cat /scratch/projects/tacc_stats/accounting/tacc_jobs_completed | grep'
alias qstat='squeue -o "%.18i %.12P %.9u %.9G %.16a %.6D %.20S %.10M %.10L %.10Q %.25V"'
alias nstat='echo A/I/O/T: Allocated/Idle/Other/Total; sinfo -o "%20P %5a %.10l %16F"'
Notes: Aliases are short cuts and are your best friend

## Slide 53: Building and Installing Software
Python
  pip install packageName --user
GitHub
  module load git
  git clone https://full/file/path
Direct Sources
  wget https://path/to/tarball.tar.gz
  tar -xvf tarball.tar.gz
Notes: Downloading from git or direct requires you then update paths to make it universally usable

## Slide 54: Ex: vcftools
$ cdw
$ mkdir vcftools
$ cd vcftools
$ git clone https://github.com/vcftools/vcftools.git
$ ./configure --prefix=$WORK/Tools
$ make
$ make install
$ export PATH=$PATH:$WORK/Tools/bin
$ vcftools
VCFtools (0.1.15)
© Adam Auton and Anthony Marcketta 2009
Notes: This is a terrible example but it’s straightforward. You have to put the path update in your .bashrc if you want it to stick once you logout

## Slide 55: What Else?
Any Software
  Build from source; get as complicated as you want
Customize login
  Modify .ssh/config on your local machine to meet your needs
Customize Editors
  Bring in outside configuration files (colors, layout, etc)

## Slide 56: .ssh/config
Host s.s2
HostName staff.stampede2.tacc.utexas.edu
User vtrue
ServerAliveInterval 60
ForwardX11 yes
Host s.ls5
HostName staff.ls5.tacc.utexas.edu
User vtrue
ServerAliveInterval 60
ForwardX11 yes

## Slide 57: Q&A
Questions Answered and Demonstrations Provided

## Slide 58: Further Information
Main Website: www.tacc.utexas.edu
User Support: www.portal.tacc.utexas.edu
Email: info@tacc.utexas.edu